## Slide 1
Verilog Sequential Circuit

## Slide 2
Operators

## Slide 3
Operators

## Slide 4
Operators

## Slide 5
Operators

## Slide 6
Operators

## Slide 7
Operators Precedence

## Slide 8
Conditional
Simple if
If else
Switch and Case

## Slide 9
Procedural Blocks
Verilog behavioural code is inside procedure blocks
initial : initial blocks execute only once at time zero (start execution at time zero).
always : always blocks loop to execute over and over again; in other words, as the name suggests, it executes always.

## Slide 10
Use of Always In Computational And Sequential Circuit
Edge-triggered circuits are described using a sequential always block

## Slide 11
Blocking vs. Non-blocking Assignments
Verilog supports two types of assignments within always blocks, with subtly different behaviors.
Blocking assignment: evaluation and assignment are immediate
Nonblocking assignment: all assignments deferred until all right-hand sides have been evaluated (end of simulation timestep)
Sometimes, as above, both produce the same result. Sometimes, not!

## Slide 12
Guideline to use
Use blocking assignments (=) for combinational
always blocks
Use non-blocking assignments (<=) for sequential always blocks
When modeling both sequential and combinational logic within the same always block, use non-blocking assignments
Do NOT mix blocking with non-blocking assignments in the same always block

## Slide 13
Example Combination Circuit (2x1 mux)

## Slide 14
GTKWAVE

## Slide 15
Example D-Flip-Flop (Sequential Circuit)

## Slide 17
Today Lab Assignments
Using always block create 2 to 4 decoder with enable. (using if else and switch and case)
Using always block create the 8x1 mux (using if else and switch and case)
Using always block create 4 to 2 encoder with enable. (using if else and switch and case)
Using always block create the 1x8 dmux (using if else and switch and case)

## Slide 18
Today Assignments
Parity checker 4x2 if more than one input is 1, the result is a don’t-care.
32-bit Adder, 32-bit Subtracter, 16-bit Multiplier (hint arithmetic operator)
Design 2x1 mux using Conditional Operator